# Microcontroller Port Assignments:

| Port A | Dir | 7 bits -- Not used. |
| --- | --- | --- |
| 0 |  |  |
| 1 |  |  |
| 2 |  |  |
| 3 |  |  |
| 4 |  | (open drain) |
| 5 |  |  |
| 6 | IM | Not brought out. |

| Port B | Dir | 8 bits, interrupting -- Interrupting Signals |
| --- | --- | --- |
| 0 |  |  |
| 1 | I | SELECT_CHANGE - Tape channel select signals have changed state since they were last read. |
| 2 | IM | FT245-RXF# (internal to module) |
| 3 |  |  |
| 4 | IM | FT245-TXE# (internal to module) |
| 5 | IM | SWVCC (internal to module) |
| 6 | I | TGO - Tape channel signal |
| 7 |  |  |

| Port C | Dir | 8 bits -- Channel State Change Requests |
| --- | --- | --- |
| 0 | I | TSETHDEN - Set Hi Density from tape channel. |
| 1 | I | TSETLDEN - Set Lo Density from tape channel. |
| 2 | I | TSETTI - Turn On TI from tape channel. |
| 3 | I | TRESETTI - Turn Off TI from tape channel. |
| 4 | I | TSETREAD - Set Read Status from tape channel. |
| 5 | I | TSETWRITE - Set Write Status from tape channel. |
| 6 |  |  |
| 7 |  |  |

| Port D | Dir | 8 bits, multiplexed -- Data Bus to 2nd Level Components |
| --- | --- | --- |
| 7:0 | I/O | DB - Bi-directional data bus. Connected to: FT245 FIFO (internal to module), Latched Select[1:6] - latched Channel Select Signals, Read Channel Direction Reg. (on analog card), Read Channel Pulse Reg. (on analog card) |

| Port E | Dir | 8 bits -- Channel Inputs and Data Bus Address Encode |
| --- | --- | --- |
| 0 | O | DBSEL[2:0] - Selects register that is to receive data from Port D data bus. Selection encodes are: 0 = FT245 FIFO 1 = SELREGOE - Select Register output enable 2 = SELRCDR - Read Channel Direction Register 3 = SELRCPR - Read Channel Pulse Register 7-4 = Read Channel Gain Controls (TBD) |
| 3 | I | TBACKWARD - Tape Channel's Backward signal |
| 4 | I | TREWIND - Tape Channel's Rewind signal |
| 5 | I | TREWUNLD - Tape Channel's Rewind and Unload signal. |
| 6 | I | TWRITELRC - Tape Channel's Write Check Character signal. |
| 7 | I | TWRITEPULSE - Write Pulse from tape channel. |

| Port F | Dir | 8 bits -- Data In from Read Channel and Echo Pulse |
| --- | --- | --- |
| 6:0 | I | TWRITEDATA - Tape Channel Write Data. |
| 7 | O | WRITEECHO -- Write Echo Pulse |

| Port G | Dir | 5 bits -- Strobe Signals |
| --- | --- | --- |
| 0 | O | SELSTROBE - Select Register Write Strobe |
| 1 | OM | FT245-RD# (internal to module) - Read next byte from FIFO. |
| 2 | OM | FT245-WR# (internal to module) - Write byte into FIFO. |
| 3 | O | ANALOGSTRB - Write strobe to the Analog Module |
| 4 |  | FT245-SNDWUP |
| 5 |  |  |

| Port H | Dir | 8 bits -- Virtual Drive Configuration |
| --- | --- | --- |
| 0 | O | MOD2 - Ready Mod 2 |
| 1 | O | MOD4 - Ready Mod 4 |
| 2 | O | MOD5OR6 - Mod 5 or 6 |
| 3 |  |  |
| 4 |  |  |
| 5 |  |  |
| 6 |  |  |
| 7 |  |  |

| Port J | Dir | 8 bits -- Virtual Drive State |
| --- | --- | --- |
| 0 | O | SELECTED - The Adapter is selected |
| 1 | O | READY - The Adapter is mechanically and electrically ready. |
| 2 | O | WRITE - The Adapter is in Write mode. |
| 3 | O | TAPEIND - The drives Tape Indicator (TI). |
| 4 | O | HIDENSITY - The drive is in Hi density write mode. |
| 5 | O | MODULE_LED# , TRIGGER_ANLZR |
| 6 | O | LOADPT - The drive's tape is at the load point. |
| 7 | O | REWINDING - The Tape is rewinding. |